| Press release wpi 616 / 0818 Area: Position sensors Safety that attracts! Magnetically-coded sensors. Essen, August 2018 – The new magnetically coded sensors from ifm are predestined for non-contact monitoring of movable guards, e.g. doors. The devices from the MN2 and MN5 series can be activated from different directions, which ensures easy and flexible installation. Concealed installation behind stainless steel or aluminium allows enhanced tamper prevention. Information according to the CB241 position paper of ZVEI for the classification of safe electronic 24 V interfaces is available. Maximum safety The combined sub-system consisting of a magnetic sensor of the MN20xS / MN50xS series and an ifm evaluation unit, e.g. G1501S or the SmartPLC of the AC4x2S series, meets the requirements up to PL e to ISO 13849-1, SILCL 3 to IEC 62061 and SIL 3 to IEC 61508. The linked sub-system was certified by TÜV NORD to simplify the conformity assessment of a safety function according to the machine guideline. The certificate can be downloaded. Protective cap for reliable installation The supplied protective caps of the MN2 family can be used once to cover the mounting screw, which allows to discover any defeating attempt. Easy connection Various connection versions with cable, M8 connector (4-pin) and M12 connector (4-pin) provide a standardised connection. They allow series connection and easy identification for the types with signal contact. wpi_616_print.jpg Magnetic sensors for movable guards For text / pictures please go to: https://www.ifm.com/de/en/de/company/technology | Contact ifm electronic gmbh Friedrichstr. 1 45128 Essen www.ifm.com Phone: 0201 / 24 22-0 Fax: 0201 / 24 22-1200 Email: presse@ifm.com Dipl.-Ing. Andreas Biniasch Technical Writing Tel. 0201 / 24 22-1425 andreas.biniasch@ifm.com |
| --- | --- |